## Slide 1
GEER 2019
Carl Fitz1,2,3
Mark Rains2
Hilary Flower2,4
Evelyn Gaiser3
1EcoLandMod, Inc.
2Univ. South Florida
3Florida International Univ.
4Eckerd College
Tortoise or Hare? Landscape Hydro-Ecological Interactions
From Presses (Sea Level Rise) and Pulses (Freshwater flows)
In the Coastal Everglades
Some of the FCE &
related models

## Slide 2: ELM Design: Integrating ecological interactions
  Ecosystem model, integrating dynamic processes of hydrology, biogeochemistry, & plant biology
  Arrows denote flows of carbon, water, & phosphorus, and information feedbacks among modules

## Slide 3
ELM Design: Pattern-process spatial interactions
  Landscape pattern (of habitats) affects local ecosystem processes
  Processes affect landscape pattern (via habitat succession)
  Canals/rivers represented by exact vectors, dynamic canal/river-marsh interactions; managed flows at point water control structures
  Integrated surface-ground water exchanges

## Slide 4
ELM skill, refinement
Peer reviews over past 20+ years
  Research journals: (Ecol Model; Restor Ecol; Crit Rev Env Sci Tec; Sust Water Qual Ecol; …)
  CERP-application review panels: (Mitsch et al. Independent Panel; CERP Interagency Modeling Center Panel; USACE certification)
Updating-refining to new ELM v3.0 (work in progress)
  Extending Period-Of-Simulation (was thru 2000, now 2005, soon 2015)
  Assimilating multiple new/refined data sources (esp. coastal glades)
    Maps: Habitats, soils, coastal river/creek topology, …
    FCE/other monitoring (e.g., salinity, TP, depth, …)
    FCE/other research (e.g., soil processes, macrophytes/diatoms/periphyton, net ecosystem production, …)
Skill assessment updates - run ELM-standard stats
  Have improved model skill in coastal/tidal regions, ongoing …
  1-year target for most improvements for formal update(s)

## Slide 5: This application:
Compare landscape responses among 36-yr scenarios of restoration flows and Sea Level Rise (SLR) combos
Scenario games bookends
  CERP0_std is Scenario Base, restoration flows standard
  CERP0_SLR: Annual SLR = 2 cm/yr applied to CERP0 coastal boundary; no management change/response
  CERP0_SLR_2xflow: Annual SLR = 2 cm/yr applied to CERP0 coastal boundary; ~2x CERP0 structure flows to southern glades
Simulating water management & ecology
  SFWMM managed flows (CERP0 from Everglades Foundation)
  ELM driven by SFWMM (point) water control structures, then simulates finer scale hydrology and ecological dynamics
Hydro-ecological Performance Measures
  Water depths & flow velocities
  Floc P & surface water chloride concentrations
  Soil processes
  Succession among habitats (& diatom communities; see Mazzei)

## Slide 6: Water budgets
Showing total (rain, gwater, seepage, overland, structure) inflows into freshwater component of ENP increased by ~1.2X under CERP0_SLR_2xflow vs. CERP0_SLR

## Slide 7
Everglades National Park (model subdomain)
Gulf of Mexico
Florida
Bay
Miami
FCE
SR Slough
transect
FCE
T Slough
transect
1
2
3
4
5
6
1
2
3
6
7

## Slide 8: Surface water chloride, 36yr: CERP0_std; CERP0_SLR; CERP0_SLR_2xflow
Coastal
Tidal
Freshwater
Flows

## Slide 9: Surface water chloride – end of wet season, last year of sim
CERP0
Diff: right - left
CERP0_SLR_2xflow
CERP0_SLR
CERP0
Diff: right - left

## Slide 10: Floc P concentration – end of wet season, last year of sim
CERP0
Diff: right - left
CERP0_SLR_2xflow
CERP0_SLR
CERP0
Diff: right - left

## Slide 11: P accumulation – Period of Simulation
CERP0
Diff: right - left
CERP0_SLR_2xflow
CERP0_SLR
CERP0
Diff: right - left

## Slide 12: Peat accretion – Period of Simulation
CERP0
Diff: right - left
CERP0_SLR_2xflow
CERP0_SLR
CERP0
Diff: right - left

## Slide 13: Habitat succession, end of wet season, last year of sim
reference
line
reference
line
reference
line
reference
line

## Slide 14
Summary-ELM scenario games
  Incremental SLR (~60cm/36yr) led to gradual ecosystem changes
  With standard CERP exposed to this SLR, coastal ecotone patterns of salinity, P, soil processes, and mangroves & open-water habitats moved inland
  Additional (CERP+) flows slightly counteracted this movement, depending on spatial location, flow paths
  The tortoise of SLR probably “wins”, but the hare’s additional pulses of freshwater flows pushes back to a meaningful extent

## Slide 15: ELM updating…
  Assimilating multiple monitoring & experimental results from FCE LTER program
  ELM: Extrapolate local-scale research understanding across heterogeneous landscapes & multiple decades (aka spatio-temporal integration)
  Iterative process, leading to improved models, and to refined hypotheses