## Slide 1
GEER 2021
Carl Fitz1,3,4
Rajendra Paudel2
Yogesh Khare2
Thomas Van Lent2
1EcoLandMod, Inc.
2Everglades Foundation
3Univ. South Florida
4Florida International Univ.
Landscape Soil Carbon Sequestration Under
Scenarios of Climate Change and CERP
Featuring...
Goldilocks’ View
of Soil Carbon
Flux Optima
climate scenarios
restoration scenarios
soil responses
...

## Slide 2: Goldilocks soil accumulation rates
Soil carbon sequestration/accumulation rate is excellent, truly integrative quantification of wetland functionality
“Too cold” (low rate)
Too high, or too low, water depths
reduced macrophyte production
increased soil loss under dry conditions
“Too hot” (high rate)
Too high nutrient loading
excessive macrophyte production & shading
replaced plant-animal species
“Just right” (optimal rate)
Happy periphyton, macrophytes, soils (& thus consumers)
Definition of healthy freshwater wetland
10 – 80 gC m-2 y-1

## Slide 3: ELM Design: Integrating ecological interactions
  Ecosystem model, integrating dynamic processes of hydrology, biogeochemistry, & plant biology
  Arrows denote flows of carbon, water, & phosphorus, and information feedbacks among modules

## Slide 4
ELM Design: Pattern-process spatial interactions
  Landscape pattern (of habitats) affects local ecosystem processes
  Processes affect landscape pattern (via habitat succession)
  Canals/rivers represented by exact vectors, with dynamic canal/river-marsh interactions; managed flows at point water control structures
  Integrated surface-ground water exchanges

## Slide 5
Currently not considering
horizontal carbon transport &
sedimentation/resuspension
Slough habitat depths
Ridge habitat depths
Past-results:
ELM captures these
ridge-slough soil accumulation
dynamics at century scales

## Slide 6
ELM skill, refinement
Peer reviews over past 20+ years
  Research journals: (Ecol Model; Restor Ecol; Crit Rev Env Sci Tec; Sust Water Qual Ecol; …)
  CERP-application review panels: (Mitsch et al. Independent Panel; CERP Interagency Modeling Center Panel; USACE certification)
Updating-refining to new ELM v3.2 (...still a work in progress)
  Extended Period-Of-Simulation (was thru 2000, now thru 2016)
  Assimilating multiple new/refined data sources (esp. coastal glades)
    Maps: Habitats, soils, coastal river/creek topology, …
    FCE/other monitoring (e.g., salinity, TP, depth, …)
    FCE/other research (e.g., soil processes, macrophytes, diatoms/periphyton, net ecosystem production, …)
Skill assessment updates - run ELM-standard stats
  Have improved model skill in coastal/tidal regions, ongoing …

## Slide 7: This application:
Compare landscape responses among 36-yr scenarios of future climate and future management combinations
3 Climate scenarios (drive SFWMM & ELM hydrology)
  Hist is historical climate, a replication of 1965-2000 daily rain and pET
  RCP4.5 is future climate, Representative Concentration Pathway 4.5, daily rain & pET from downscaled ensemble means of 27 GCMs
  RCP8.5, similarly, is future climate, but higher global CO2 concentrations
2 Water management scenarios (daily water control structure flows from SFWMM output, distributed via ELM fine-scale hydrology)
  ECB is Existing Conditions Base, using current infrastructure and water management practices (applied to 36 yr future)
  CERP0 is Comprehensive Everglades Restoration Plan, the full implementation of future infrastructure and water management
ELM hydro-ecological Performance Measures
  Soil carbon accumulation rate over 36 year period
  Other ELM metrics (flow/depth, TP, periphyton/diatoms, veg succession, etc) not presented here

## Slide 8
Future climate: downscaled ensemble means of
27 General Circulation Models (GCMs). See works of R. Paudel, J. Infanti
Rain – 36 yr:
RCP8.5 (&4.5) less variable than observed historical
ET – 36 yr:
RCP8.5 (&4.5) greater than observed historical

## Slide 9: Soil carbon accumulation rates – 36 yr, 2016-2051
ECB
Difference
CERP
Historical
Climate
RCP 4.5
Climate
RCP 8.5
Climate
CERP tends to increase rates, varying spatially
Spatially, rates
differ subtly
among climate
scenarios
Major point:
Visualize general similarities in patterns
(showing all rates, not just Goldilocks)

## Slide 10
Regional landscape (~million* ha) responses,
scenarios of ECB vs CERP under 3 climates
*975,650 ha: WCAs, ENP, BCNP

## Slide 11
Summary
  Relative to baseline, CERP had integrated ecological benefits under historical climate (not much “news”, other than metric itself)
  ... AND CERP practices had (apparently even higher relative) benefits under future climate (vs. historical) scenarios
  Integrated ecological dynamics may respond to significant reduction in interannual rainfall variability
  Plans include discrimination of different GCMs to resolve more of the natural rainfall variability
  ... AND to impose associated future Sea Level Rise water and salinity levels in the coastal Everglades

## Slide 12: ELM updating…
  Assimilating multiple monitoring & experimental results from Florida Coastal Everglades LTER program
  Extrapolating local-scale research across heterogeneous landscapes & multiple decades (i.e., spatio-temporal integration)